## Slide 1: Indoor localization
ZHANG YIFAN

## Slide 2: LBS（location based service）
GNSS(global navigation satellite system）GPS(USA),GLONASS(RUSSIA),Galileo（Europe）北斗（China）

## Slide 3: LBS（location based service）
Navigation，Traffic Control
Convenience Service
Social Activity

## Slide 4: LBS
Satellite | Distance | 
S1 | ρ1 | 
S2 | ρ2 | 
S3 | ρ3 | 
S4 | ρ4 | 

## Slide 5: Problems
Signals cut out by buildings
Multipath effect
Shadow effect
Other wireless device

## Slide 6: Fingerprinting based indoor localization

## Slide 7: PROCEDURE OF FINGERPRINTING BASED INDOOR LOCALIZATION

## Slide 8: MY EXPERIMENT
PREPARATION
FINGERPRINTING DATABASE
SOFTWARE
MAP
COLLECTING DATA
ONLINE
COLLECTING DATA
CALCULATION
CALCULATION

## Slide 9: SOFTWARE
WirelessMon

## Slide 10
MAP

## Slide 11: My fingerprint database
序号 | 坐标 | p2psearch | 403 | FAST | DEJURE | DORM503
1 | (0.3,1.2) | -27 | -54 | -62 | -66 | -67
2 | (0.3,2.8) | -42 | -25 | -74 | -69 | -64
3 | (0.6,0.9) | -24 | -57 | -57 | -58 | -64
4 | (2.4,6.6) | -54 | -66 | -75 | -73 | -73
5 | (0.1,6.6) | -64 | -59 | -62 | -75 | -75
6 | (0.1,-1.5) | -47 | -60 | -68 | -79 | N/A
7 | (3.2,4.2) | -48 | -60 | -75 | -79 | -75
8 | (2.4,3.2) | -41 | -45 | -65 | -60 | -66
9 | (1.5,1.7) | -28 | -45 | -64 | -62 | -68
10 | (1.8,4) | -45 | -51 | -72 | -64 | -65

## Slide 12: Online data collecting
序号 | P2psearch | 403 | FAST | DEJURE | DORM503
1 | -36 | -45 | -71 | -62 | -64

## Slide 13: Algorithm
1.NN（nearest neighborhood）
2.KNN（K-nearest neighborhood）

## Slide 14: Calculation
81 | 81 | 81 | 16 | 9 | 268 | 16.37071
36 | 400 | 9 | 49 | 0 | 494 | 22.22611
144 | 144 | 196 | 16 | 0 | 500 | 22.36068
324 | 441 | 16 | 121 | 81 | 983 | 31.35283
784 | 196 | 81 | 169 | 121 | 1351 | 36.75595
121 | 225 | 9 | 289 | #VALUE! | #VALUE! | #VALUE!
144 | 225 | 16 | 289 | 121 | 795 | 28.19574
25 | 0 | 36 | 4 | 4 | 69 | 8.306624
64 | 0 | 49 | 0 | 16 | 129 | 11.35782
81 | 36 | 1 | 4 | 1 | 123 | 11.09054
For NN the result is （2.4,3.2）
For k-NN， if k=2，the result is（2.0,3.6）
if k=3， the result is （1.9，2.96）
The actual coordinate is （1.8,3.0）

## Slide 15: Problems
Facility problems
1.1 wirelessmon
1.2 laptop
1.3 router
1.4 other device’s influence
Not enough fingerprint database

## Slide 16
Thank you