## Slide 1: Spatio-temporal Gaussian Process Based Radio Map Reconstruction
韩雨桐 2016/6/3

## Slide 2: Road Map
Raise the Question
Gaussian Process
Our Model
Future Work

## Slide 3: Introduction
Wi-Fi has been used in indoor localization
RSSI-Based Localization
Triangulation
Fingerprint
Notes: Over the past decade, the increasing use of Wifi technology has been implemented in real-world location based applications, especially in localizing clients holding
mobile devices in indoor environments.
There are many algorithm to solve this problem, one of the most popular solution is based on the RSSI
from multiple access points, which also abbreviated as AP.
Wi-Fi triangulation’s goal is to map RSSI as a function of distance. This method requires a steep linear characterization curve in order to be properly implemented. Functions
describing these curves are then used with live RSSI values as
input to generate an (x,y) location prediction.

## Slide 4: Fingerprinting
Offline Phase
Collect RSS from AP
Result in a radio map
Online Phase
Get the RSS of mobile clients from AP
Search radio map to estimate client’s location
Notes: Fingerprint wireless localization techniques is performed on two phases;
During the offline phase, the signal strength received from the access
points at selected locations are stored in a database, resulting in a radio map.
During the online phase, the system use the signal strength samples of mobile clients from the
access points to search radio map to estimate the client’s location

## Slide 5: Fingerprinting
Offline Phase
Collect RSS from AP
Result in a radio map
Online Phase
Get the RSS of mobile clients from AP
Search radio map to estimate client’s location
Notes: Fingerprint wireless localization techniques is performed on two phases;
During the offline phase, the signal strength received from the access
points at selected locations are stored in a database, resulting in a radio map.
During the online phase, the system use the signal strength samples of mobile clients from the
access points to search radio map to estimate the client’s location

## Slide 6: Radio Map example
A radio map of the one of the Routers
Color indicates RSS
Notes: Here is a visualization example of radio map,
This is the radio map of one of the routers,
We divide the whole space into several block, as the picture shown
And the color of each blocks indicates the RSS of the access point
Also as this Radio map shows us, if we want to construct this kind of radio map in our classroom, a place about 100 square meters. We have to collect the RSS value in at least 100 blocks. So, how about the place we want to localize is a supermarket, or a big factory ?

## Slide 7: Problem of fingerprinting localization
Difficult to construct the radio map of large environment
True radio map change over time
Hardware device variance
Notes: So the first problem is when we want to localize in a large environment, we may pay a large effort to construct the radio map of the environment.
Another challenges with fingerprints techniques is that they are vulnerable to several dynamic factors in
locations.
The first kind of factors are inherent factors, such as wireless channels changes over time when the client is standing at a fixed location.
Another kind of factors are external factors, such as hardware device variance problem: the device (training device) used to construct radio maps during the offline phase
differ from the tracking devices used during the online phase, the variance between these two device can make us collect different fingerprint at same position in the same environment.
So the last two factors will both influence the accuracy of our localization.
To handle such factors it is imperative to first understand
the impact of these factors. The experiments described later
indicate how these factors influence the accuracy of localization. Further, we also consider these factors into our indoor
localization system model.

## Slide 8: Our aim
Use part of the data to reconstruct the whole radio map
Use these data to predict the radio map
Construct the transfer function model between different device

## Slide 9: Road Map
Raise the Question
Gaussian Process
Our Model
Future Work

## Slide 10: Motivation
Given a training set
How to calculate the output for a new input
Linear regression?
– Least Square Method
Nonlinear regression?
-- Gaussian Process

## Slide 11: Definition
Assume obey multivariate Gaussian Distribution
Where

## Slide 12: Definition
Covariance Function ---- kernel
Noise

## Slide 13: Regression
For new input
where

## Slide 14: Regression
For new input
We get
Mean：
Variance：

## Slide 15: Find Parameters
Using Maximum Likelihood
Max

## Slide 16: GPR example

## Slide 17: Road Map
Raise the Question
Gaussian Process
Our Model
Future Work

## Slide 18: Transfer Function
Device A is the standard device.
Device B get the RSS from the same AP
Notes: Suppose device A is the standard device.In a given location, device A and another device B all get the RSS from the same AP. We suppose that the RSSA is the standard value, and RSSB should be mapped to RSSA collected by device A.

## Slide 19: Transfer Function

## Slide 20: Spatio-temporal model

## Slide 21: Road Map
Raise the Question
Gaussian Process
Our Model
Future Work

## Slide 22: Future work
Using new data to evaluate our model
Combine the GPR model

## Slide 23
Q & A