## Slide 1: Cooperative Relay with MIMO nodes
Zhu Yumeng
05/16/2014

## Slide 2
Outline
Background : cooperative relay
MIMO relays
Future Work

## Slide 3
Cooperative Relay
In a cognitive radio network, when the traffic demand and spectrum resource availability are largely mismatched, it cannot fully utilize spectrum resource and fulfill secondary users’ demands.
AP
S1
S2
150Kbps
50Kbps
[1,3,4]
[1,2]
[2,3,4]
Data rate:100Kbps
AP
S1
[1]
S2
[3]
Notes: Two secondary end users S1 and S2 want to receive data from the AP. The numbers on the dashed lines indicate the average traffic demand of the users from AP. We assume that each common channel between any pair of nodes can provide 100Kbps date rate.
In the traditional transmission,S1 uses up the channel one and receives 100 Kbps while S2 receives 50Kbps because of its small traffic demand.

## Slide 4
Cooperative Relay
Cooperative relay scheme
AP
S1
[1]
S2
[3,4]
CH1
CH2
CH3
CH4
AP
S1
S2
own data
data for S1
Notes: Improvement is possible if we introduce cooperative relay
Scheme including two time slots with equal time interval

## Slide 5
Cooperative Relay
Cooperative relay scheme
CH1
CH2
CH3
CH4
AP
S1
[1]
S2
[2]
AP
S1
S2
own data
data for S1
Notes: Both of the demands are fulfilled.

## Slide 6
Outline
Background : cooperative relay
MIMO relays
Future Work
Notes: Nowadays, most of mobile devices, which usually function as secondary end users have more than one antenna, so we introduce MIMO relays.

## Slide 7
MIMO
Compared to single-input single-output(SISO), multiple-input multiple-output(MIMO) techniques can provide high spectral efficiency and increase channel capacity substantially through multiple spatial channels without need of the additional spectrum.
  spatial multiplexing
  A high rate signal is split into multiple lower rate streams and each stream is transmitted from a different transmit antenna in the same frequency channel.

## Slide 8
MIMO Relays
AP
D1
R
D2
Cooperative relay topology
Constraints:
  One node can have only one relay;
  One relay can serve only one node;
  When one node is served by a relay, this node cannot be the relay node of another node.
One relay can serve more than one node;
Notes: Depend on the number of antennas

## Slide 9
MIMO Relays
Problem formulation
  Denote the cognitive radio network as a set of nodes
  The spectrum is channelized into channels with equal bandwidth and guard bands.
  Use a 0-1 variable to denote the channel availability : indicates the channel at node is available
  Use to denote the set of direct links : means there exists a direct link between the two nodes
Notes: V0 the secondary AP node
Ui MIMO nodes
Divide channels into two parts
K1 used by regular nodes
K2 used by MIMO nodes

## Slide 10
MIMO Relays
Cont’d
    Use to denote the demand of transmission that would like to receive from (AP)
    Assume the transmission rate of each link in every channel is identical, which is denoted by
  Define a 0-1 matrix to express the relay relationship: means that performs as relay node for
  Use to denote the channel assignment: if channel is assigned to link for data transmission
Notes: X=1 if channel k is assigned to link eij

## Slide 11
MIMO Relays
Additional denotations
  Use a set of nodes to denote MIMO nodes, a set of numbers to denote the number of MIMO nodes’ antennas
  Use a 0-1 variable to denote the channel availability : indicates the channel at node is available
  Use to denote the set of direct links : means there exists a direct link between the and
  Define a 0-1 matrix to express the relay relationship: means that performs as relay node for
  Use to denote the channel assignment: if channel is assigned to link for data transmission
Notes: V0 the secondary AP node
Ui MIMO nodes
Divide channels into two parts
K1 used by regular nodes
K2 used by MIMO nodes

## Slide 12
MIMO Relays
Four categories:
  A receiver without a relay’s help
  Acts as a relay
Notes: Remaining nodes make up a conditional cooperative

## Slide 13
MIMO Relays
Cont’d
  Receive data with the help of a regular relay
  Receive data with the help of a MIMO relay
Notes: Remaining nodes make up a conditional cooperative

## Slide 14
MIMO Relays
Unified format:
Given demands ,to compute a feasible relay selection and channel allocation scheme so that total system throughput is maximized.
Formulate the problem:

## Slide 15
MIMO Relays
Proposition
  If one user’s demand is not fulfilled, it will not act as a relay to help others because this will definitely decrease the total throughput of the whole system.
  Nodes partition
  If we do not involve relay transmission in the network, the problem can be simplified as
  Divide nodes: potential destination and potential relay
Notes: A max flow problem can be solved in polynomial time

## Slide 16
MIMO Relays
  Total capacity
    denotes the number of the channels used by total regular nodes, for MIMO nodes
Secondary AP node
MIMO node
Potential destination
Potential relay
subsystem
Notes: Explain the expression in detail
Different colors to represent different kinds of nodes
The algorithm aims to make full use of channel capacity ,so the total capacity in some way determines the throughput.
That means the channels will satisfy MIMO relays’ demand first, which makes C as large as possible.

## Slide 17
MIMO Relays
Subsystem
  How to choose nodes from potential destination to be served by MIMO relays?
Two categories:
  A receiver without MIMO’s help
  Receive data with the help of a MIMO relay
Notes: X=1 if channel k is assigned to link eij

## Slide 18
MIMO Relays
Given demands ,to compute a feasible relay selection and channel allocation scheme so that total system throughput is maximized.
Formulate the problem:
Unified format:
Notes: Subject to 受约束

## Slide 19
MIMO Relays
Remaining system
Formulate the problem:
Notes: Subject to 受约束

## Slide 20
Outline
Background : cooperative relay
MIMO relays
Future Work

## Slide 21
Future Work
Build a MIMO-OFDM system acting as MIMO relays
USRP 2920
Notes: Relay-assisted D-OFDM

## Slide 22: Thank you !