## Slide 1
Pedometer Placed in the Pocket
Lecturer: Junwei Lu
Notes: Hello everyone. Today I’ll talk about my work in this semester, which is about pedometer.

## Slide 2
Previous Work
1
Pedometer Placed in the Pocket
3
Future Work
5
Outline
Notes: I’ll introduce my work in three parts, which are:

## Slide 3
Previous Work
Basic scenario:
  The phone is held by hand horizontally.
Basic approach:
  Utilize the acceleration on the z-axis.
  Detect the peak and valley of the
  processed waveform obtained from
  the accelerometer.
Notes: First, let me introduce the previous work that’s done by Zhangjialu et al.

## Slide 4
The Preprocess of the Data
The waveform is full of jitter.
Low-pass filter:
  y
Moving average.

## Slide 5
The Preprocess of the Data
Raw data
Processed data

## Slide 6
Peak Detection
Magnitude threshold
Temporal threshold

## Slide 7
Previous Work
1
Pedometer Placed in the Pocket
3
Future Work
5
Outline

## Slide 8
Pedometer Placed in the Pocket
Basic scenario:
  The phone or accelerometer is placed in the pocket.
What is the critical indicator of a step?
Rotation of leg!
Utilize gyroscope data.

## Slide 9
Waveform of Angular Velocity on X-Axis
After walking 50 steps in a constant speed in a straight line, the result returned by the algorithm is 51.

## Slide 10
Complex Circumstances
Different people, different rotation magnitude.
Different walking mode.
Temporal threshold and magnitude threshold should be set adaptively!

## Slide 11
Adjust Magnitude Thresholds Adaptively
, defined as the magnitude standard deviation for the recent K samples.

## Slide 12
Adjust Magnitude Thresholds Adaptively

## Slide 13
Adjust Temporal Thresholds Adaptively

## Slide 14
Previous Work
1
Pedometer Placed in the Pocket
3
Future Work
5
Outline

## Slide 15
Future Work
Finding a good parameter for the adaptive algorithm to achieve high accuracy.
Utilizing the data of other sensors to help judging whether walking and judging the change of device pose.

## Slide 16
References
计步器pattern分析, Jialu Zhang, Yucheng Xing.
Step Detection Robust against the Dynamics of Smartphones, Hwan-hee Lee, Suji Choi and Myeong-jin Lee

## Slide 17
Thanks！

## Slide 18
Q&A