## Slide 1: A Location System Based on RFID
5130309748 Neng Li
2016/5/30

## Slide 2: Outline
Introduction
System
Experiment

## Slide 3: Introduction of RFID
Radio Frequency Identification
  Use a radio signal to identify a specific target and read data.
  Type of tags: active or passive
  Infer distance from phase.
Impinj R420
Reader:
Antenna:

## Slide 4: Advantages of RFID
Compared with WIFI location system and bluetooth location system
  Higher accuracy
  Passive tag
  Lower cost
  High transmission rate

## Slide 5: Outline
Introduction
System
Experiment

## Slide 6: Selection of Frequency
UHF RFID System
  From 300MHz ~ 1GHz
  High transmission rate (100kbps)
  3~10m read range (for passive tag)
Microwave RFID System
  2.45GHz
  High transmission rate (100kbps)
  2m read range (for passive tag)
  Easily be affected by environment

## Slide 7: ISO 18000-6
ISO 18000-6 is a standard for UFH RFID system.
Frequency of ISO 18000-6 standard : 860MHz~960MHz
Reason:
  860MHz ~ 960MHz can avoid WIFI’s interference
  ISO 18000-6 has a suitable read range

## Slide 8: Signal Collision in RFID
Signal collision from readers
  When multiple readers read tag simultaneously, the reader can’t judge which response is the one it needs.
Signal collision from tags
  The incidence of multiple responses from multiple tags reaching simultaneously to the antenna prevents it of identifying each response individually.

## Slide 9: ALOHA algorithm

## Slide 10: EPC tags
EPC tag is a read-only tag and can be passively powered.
Each tags contains the identifying information.
Size of EPC tag is quite small

## Slide 11: Outline
Introduction
System
Experiment

## Slide 12: Refer distance from phase
Chart: Phase-Distance(921.625MHz)
| 2 | 4 | 5 | 6 | 8 | 9 | 10 | 11 | 12 | 14 | 15 | 16 | 18 | 20 | 22 | 24 | 26
 | 0.89674 | 6.0808 | 5.2952 | 4.5943 | 3.4393 | 3.2401 | 2.8279 | 2.5038 | 2.1736 | 1.7343 | 1.7687 | 1.542 | 0.86196 | 0.29415 | 0.066739 | 4.9274 | 3.5244

## Slide 13: Future work
Use different frequency to locate a tag away from wavelength.
Improve the accuracy when more than one frequency are used.

## Slide 14
Thank you
Q&A