## Slide 1
A Brief Introduction of Indoor
Localization Algorithms
5130309750 Chen Hongkun
2016/5/23

## Slide 2
Introduction
Indoor Localization
Range-based
TOA
Fingerprint
UWB
TDOA
RSSI
AOA
GPS
Bluetooth
ZigBee
Wi-Fi
Range-free
Structure of Indoor Localization Algorithms
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 3
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Time of Arrival
r
Sometimes called Time of Flight, it is the travel time of a radio signal from a single transmitter to a remote single receiver
The Ap’s position is already known, so the target is on a circle with radius r.
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 4
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Time of Arrival
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 5
TOA
AOA
RSSI
Fingerprint
Lab
TDOA
Time Difference of Arrival
Other than absolute distance, it measures the difference
The receiver(cellphone) is on a hyperbolic curve
Locate the target by finding the intersection
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 6
TOA
AOA
RSSI
Fingerprint
Lab
TDOA
Time Difference of Arrival
Question:
How to get the value of TDOA (Distance between R1 and T, R2 and T)?
Answer01:
Using TOA
Answer02:
Using……?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 7
TOA
TDOA
RSSI
Fingerprint
Lab
AOA
Angle of Arrival
It measures the angle
Receiver is on a line
Finding the intersection
How to measure the angle ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 8
TOA
TDOA
RSSI
Fingerprint
Lab
AOA
How to measure \theta ?
d
‘d’ is what we have measured in TDOA
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 9
TOA
AOA
RSSI
Fingerprint
Lab
TDOA
Time Difference of Arrival
Question:
How to get the value of TDOA ?
Answer01:
Using TOA
Answer02:
Using……
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 10
TOA
TDOA
RSSI
Fingerprint
Lab
AOA
Angle of Arrival
We can measure phase difference
d
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 11
TOA
TDOA
AOA
Fingerprint
Lab
RSSI
Received Signal Strength Indicator
DESCRIPTION:
A measurement of the power
RSSI declines with distance
3. Map between RSSI and distance
PROBLEM:
Unstable, inaccuracy
IMPROVEMENT:
Will 2 Aps or more improve the accuracy of location ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 12
TOA
TDOA
AOA
RSSI
Lab
Fingerprint
STEPS:
  Record a vector of RSSIs (or other parameters) at a specific location
  Compare the measuring vector with recorded vectors and find the optimum one
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 13
TOA
TDOA
AOA
RSSI
Lab
Fingerprint
STEPS:
  Record a vector of RSSIs (or other parameters) at a specific location
  Compare the measuring vector with recorded vectors and find the optimum one
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 14
TOA
TDOA
AOA
RSSI
Lab
Fingerprint
Improvement:
  Mean value model
  Gaussian model
Key Part.
Choose a good matching method.
For example.
Euclidean distance
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 15
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Algorithm: | Fingerprint-based
Size of room | 4m* 5m
Number of samples | 15
Number of Ap | 5
Accuracy | 3m
What we have done in the lab:
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 16
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Problem 1. Multipath
Q: We suppose the two incoming signals are parallel here, but what if there are more or they are not parallel ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 17
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Problem 2. Package Detection Delay
Q: Did the package detection delay be counted into TOA ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 18
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
inaccuracy
Problem 3. Synchronization
Q: How to make sure the synchronization has a precision of nanosecond level ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 19
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Problem 4. Phase difference
Q: Can we distinguish cases when and ?
When ……
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 20
TOA
TDOA
AOA
RSSI
Fingerprint
Lab
Problem 5. Intersection
Q: What if there are more than three Aps in which case there are more than one intersection ?
Notes: You can add your own categories and points values to this game board. Enter your questions and answers in the slides we’ve provided.
When you’re in slide show view, select the underlined text to go to that question, then move to the answer slide. Use the left triangle to return to this game board slide.

## Slide 21
Q & A
THNAK YOU