## Slide 2: WiFi is a powerful sensing medium
Gait Identification
Gesture Recognition

## Slide 3: Limitations
Require collecting training data in all sites
Only support for a handful of users
Notes: 同一个人、同一手势在不同地方的特征表现非常不同（原因：multipath effect）。图为同一个人的手势在两个不同地点的特征。收集数据需要耗费大量时间
User数目增多时，准确率下降明显。

## Slide 4: Goals
Scaling to new environments
Consistent performance for larger problem sizes
Notes: 仅在一个地点收集数据，但是通过一些方法得到多个环境下的模型，达到跨站点的效果
分类的类别数增加依然能保持很好的效果（步态识别中的用户数目，手势识别中的手势数目）

## Slide 5: Roaming WiFi metrics
y = f(x)
Translated signal metrics for site B
Input signal metrics
for site A
Roaming model
Learning how does the environment affect the WiFi signal
Notes: 不同地点的数据扩展

## Slide 6: Using multiple sensing models
y = g(x)
Sensing model to use
Input WiFi signal
Expert selector
Dynamically choose which sensing model (expert) to use
Notes: 问题规模增大时的解决方案：采用expert selector选择不同的模型

## Slide 7: How do the two parts work together?
Roaming model
WiFi data
WiFi training data for new sites
Notes: 1. 训练一个roaming model，offline

## Slide 8: Model Input
WiFi data
Noise Removal
Feature Selection

## Slide 9: Artificial neural network based data roaming
Roaming model
WiFi data
WiFi training data for new sites

## Slide 10: Roaming model
7-layer MLP
Training data
  data collection site  deployment site
  Data collection time cost ~14 hrs
Transfer learning
  Shared params (first few layers) between ModelA_B and ModelA_C
  Reducing data collection cost largely

## Slide 11: Classification based model selection
Roaming model
WiFi data
WiFi training data for new sites

## Slide 12: Sensing model chosen based on input signal characteristics
Sensing model 1
Sensing model 2
Sensing model N
…
Sensing model i
Translated WiFi signals
kNN classifier

## Slide 13: Prior art
Gait Identification
Gesture Recognition
WiWHO
WiFiU
WiG
WiAG
Tens of participants
Handful of gestures

## Slide 14: Evaluation Setup
Environments: 3x sites: low, medium and high multipath
Activities: Gait identification (100 users) and gesture recognition (40 gestures)
Wireless channel metrics: CSI and RSSI

## Slide 15: Consistently good performance

## Slide 16: Roaming WiFi data improves the performance

## Slide 17: Conclusion
Problem: Wifi sensing is great, but limited to small-scale deployments
Solutions: Machine learning for roaming training data and scalable performance
Results:
  4x improvements on accuracy
  much larger problem sizes

## Slide 18: Thank you