## Slide 1: Your Microphone Array Retains Your Identity: A Robust Voice Liveness Detection System for Smart Speakers
Yan Meng1, Jiachun Li1, Matthew Pillari2, Arjun Deopujari2, Liam Brennan2, Hafsah Shamsie2, Haojin Zhu1, and Yuan Tian2
1Shanghai Jiao Tong University
2University of Virginia
August, 2022
1
USENIX SECURITY 2022
Notes: 活跃度检测； 基于语音系统。
和之前文章的相似度；

## Slide 2: OUTLINE
Background
Motivation System Design
Evaluations
Discussions Conclusion
2

## Slide 3: 1
Background
3

## Slide 4: Smart Home
A typical application of cyber physical system (CPS)
Undergoing rapid growth of market size
Global Market1
$84.5 Billion（2021） $138.9 Billion（2026）
1. Markets and Markets Research, Smart Home Market with COVID-19 Impact Analysis by Product.
A typical example of smart home
4

## Slide 5: Voice Interface
The primary user interface in smart home
Smart speakers with multiple microphones
Cortana Google Now
Typical applications
Siri
Alexa
Voice Interface Hardware
Standalone microphone
Smart speakers
5
Notes: 语言接口

## Slide 6: Threats Faced by Voice Interface
Suffering from voice spoofing due to its broadcast nature
Typical attacks: replay attack, hidden voice, inaudible attack
Classical replay attack
Hidden voice attack
（Carlini et al, Security’16）
Dolphin attack
（Zhang et al, CCS’17）
Attacker Machine Replay
6
Hidden voice:人类听众无法理解但被设备解释为命令的隐藏语音命令
Notes: 智能音箱等具有广播的性质(任何人可以接入)，容易遭受攻击
重放攻击、

## Slide 7: Thwart Voice Spoofing: Liveness Detection
Detection Principle: Authentic and spoofing voice commands are generated by real human and electrical device respectively.
Liveness detection: detecting factors related to human
Voice Command
User
VCS
Openness nature
Authentic
Spoofing
7
活体检测是提升智能音箱等安全的主要方法
Notes: 阻止语音欺骗:活体检测。 Spoof: 电子欺骗

## Slide 8: Existing Liveness Detection Schemes
Leveraging image, accelerator, or ultrasonic as the second factor.
Limitations: requiring carrying device, incurring user’s burden
Two-factor Authentication
Passive Liveness Detection
Image
Chen et al INFOCOM’17
Ultrasound
Zhang et al
CCS’17
Acceleration
Feng et al MobiCom’17
Notes: 已有的活体检测方法：双因子认证。
已有方法都需要额外设备。

## Slide 9: Existing Liveness Detection Schemes
Different sound
generation models
Ahmed et al.,（0~10kHz） USENIX Security’20
Yan et al., fieldprint
CCS’19
Passive detection: only utilizing collected voice samples
The voice spectrums from authentic user and spoofing are different
Features: spectrum (mono); Fieldprint (dual-channel)
𝑀1
𝑀2
9
Two-factor Authentication
Passive Liveness Detection
Notes: 其他被动检测的方法，尝试去分辨构造模型、低频特性、

## Slide 10
Yan et al., fieldprint
CCS’19
Notes: 利用声场的概念

## Slide 11: Existing Liveness Detection Schemes
Unstable spectrum characteristics (mono channel)
Required fixed gestures (dual channel)
Limitations Faced by Passive Detection
Location A
Location B
Fixed gestures
Unstable spectrums
Can we design an effective and robust passive liveness detection scheme?

## Slide 12: 2
Motivation

## Slide 13: Microphone Array Based Solution
𝑀1
𝑀𝑁
𝑀𝑁−1
𝑟
𝑆0 (𝐿, 0)
𝑑
2
𝑦 𝑀2
𝑥
𝜃
2𝜋/𝑁
𝑑1
𝑂
Smart speakers usually have the microphone array
Multi-channel audios have more diversity
𝑀1
𝑀2
Smart phone: pair
Single microphone
Smart speaker: array
Microphone array
Notes: 具体来讲，可以利用麦克风阵列的特性

## Slide 14: Array Fingerprint
Extracting feature from multiple channel audios
Better robustness
Rotate 𝟗𝟎∘
Rotate 𝟏𝟖𝟎∘
Dual channel Feature
Array Fingerprint
麦克风阵列特征具有旋转不变等更稳定的特性

## Slide 15: Validation of Array Fingerprint
Effective to distinguish authentic user and spoofing devices
Preliminary实验：发现不同设备上，特征均比较稳定。

## Slide 16: 3
System Design

## Slide 17: System Overflow of ArrayID
ArrayID consists of four modules:
  Data Collection
  Pre-processing
  Feature Extraction
  Attack Detection

## Slide 18: Data Collection and Preprocessing
Microphone array
  Matrix Creator
  Seeed ReSpeaker Core V2
Preprocessing
  STFT
Direction Detection
Preprocessing module
Feature extraction
Attack detection
Data collection module
Spectrograms from first, third and fifth microphones

## Slide 19: Feature Extraction
Calculating array fingerprint
Preprocessing module
Feature extraction
Attack detection
Data collection module
Meshing
Calculating

## Slide 20: Feature Extraction
Preprocessing module
Feature extraction
Attack detection
Data collection module
Array fingerprint
Calculating array fingerprint
Extracting more features
  Spectrogram distributions
  LPCC
Distributions from whole audio channels

## Slide 21: Attack Detection
Classification model:
  lightweight feed-forward back- propagation neural network
  Network, 3 layers, Size 64/32/16
Preprocessing module
Feature extraction
Attack detection
Data collection module

## Slide 22: 4
Evaluations

## Slide 23: Dataset Collection
Hardware setup
  Data collection device: Matrix Creator, Seeed ReSpeaker Core v2
  Spoofing devices: 14 different devices
Microphone array
Part of employed spoofing devices

## Slide 25: Dataset Collection
20 types of voice commands from 20 users
10241 authentic commands，22529 spoofing samples
Metrics：Accuracy；FAR；FRR；EER
Voice command samples
Turn on Bluetooth.
Remind me to buy coffee at 7 am.
Open music player.

## Slide 26: Performance
Performance on our collected dataset
  Two-fold cross-validation
  Accuracy: 99.84%, EER: 0.17%.
  FAR: 0.05%; FRR: 0.39%
ReMasc dataset, Accuracy is 97.78%
Time overhead
  6-channel: 0.12 seconds; 8-channel: 0.38 seconds
  Desktop with Intel i7-7700T CPU and 16 GB RAM

## Slide 27: Impact of Various Factors
ArrayID is robust to the following factors:
Distance
Direction
Spoofing devices
Environment
User movement
Training Distance (m) | 1.2 | 1.8 | 2.4
Accuracy (%) | 99.41 | 99.53 | 99.66
EER (%) | 1.11 | 0.93 | 0.69
100
99.5
99
98.5
Front
Left
Accuracy (%)
1.5
1
0.5
0
Right Back Front
Impact of distance
EER (%)
Left
Right
Back
Impact of direction

## Slide 28: 5
Discussions

## Slide 29: Impact of Noise
Performance degrades when the noise increases.
Experiment setup
98.8
100
91.36
92.1
86.3
100
90
80
70
45
50
55
60
65
Accuracy (%)
30
20
10
0
45
50
55
60
65
EER (%)
Performance
27

## Slide 30: Impact of Modulated Attack
Effective but unstable when handling modulated attack.
Processing via Inverse Filter
Similar with Authentic
Still robust
Spoofing Device | Echo | iPad | Mi
Accuracy (%) | 100 | 92.74 | 97.29
Still an open problem
Notes: 调制以后的信号，效果不好。

## Slide 31: Training Requirements
ArrayID requires audio samples for training classifier
Performance degrades when no training samples
No Training Hurdles remains an open problem
Training Requirements

## Slide 32: 6
Conclusions

## Slide 33: Conclusion
Summary:
  Propose ARRAYID for thwarting voice spoofing attacks without any extra devices.
  Propose a robust liveness feature array fingerprint.
  Proved to be effective and robust to various factors.
Future Work
  Improve the performance under strong noises.
  Thwart more advanced attacks.
  Achieving no training hurdles.
Notes: 消除/阻止

## Slide 34
Mic Array for sensing, e.g., AudioSense
Smart Speaker Array for, e.g., fall detection
Discussion

## Slide 35: Conclusion
Thank you!
Yan Meng: yan_meng@sjtu.edu.cn Haojin Zhu: zhu-hj@sjtu.edu.cn